## Slide 1
II. Modeling procedure
We consider 9,023 streamgauges with at least 30 years of observations available.
Streamflow database
USGS (CONUS): 4,596 basins
ADHI (Africa): 362 basins
HRS (Australia): 467 basins
GSIM (Others): 3,598 basins
Climate type
Tropical Temperate Polar
Arid Cold
FloodMagnitude_v1.4/01_Covariate_selection/

## Slide 2
II. Modeling procedure
We consider a local water year that starts in the season with the lowest median of seasonal maxima among the four seasons.
J | J | A | S | O | N | D | J | F | M | A | M | J | J | A | S | O | N | D | J | F
Calander year: 2000
Water year: 2000
J | J | A | S | O | N | D | J | F | M | A | M | J | J | A | S | O | N | D | J | F
J | J | A | S | O | N | D | J | F | M | A | M | J | J | A | S | O | N | D | J | F
e.g.) Driest season: Jun-Aug (JJA)
e.g.) Driest season: Sep-Nov (SON)
e.g.) Driest season: Mar-May (MAM)
…
Calander year: 2000
Calander year: 2000
Water year: 2000
Water year: 2000

## Slide 3
II. Modeling procedure
We employ the skill score (SS) decomposing it into potential skill and bias to evaluate the model performance.
Bradley A.A. et al. (eds), Handbook of Hydrometeorological Ensemble Forecasting, Springer, Berlin, Heidelberg, 2016
Potential Skill
Unconditional Bias
Conditional Bias
correlation between the forecasts and observations
: standard deviation of the forecasts (observations)
: mean of the forecasts (observations)

## Slide 4
II. Modeling procedure — (1) Climate driver selection
Instead of using all observations, we apply a training – validation approach to identify primary climate drivers, enabling more robust peak discharge predictions, especially for extrapolation.
(1) Randomly split the entire years into training (80%) and validation (20%) years.
Training years (80%)
Validation years (20%)
(2) For each season, fit all possible statistical models based on training years and select the best model based on the SBC.
Pconc (Pprev): basin-averaged seasonal precipitation for the
concurrent (previous) season of interest.
Tconc (Tprev): basin-averaged seasonal temperature for the
concurrent (previous) season of interest.
<DJF>
M1:
M2:
M3:
M4:
…
Training years (80%)
M2 (Smallest SBC)
(3) Once we have four seasonal models, simulate annual maximum values for the validation years through Monte Carlo simulation (5,000 times).
Validation years (20%)
DJF: M2
MAM: M1
JJA: M4
SON: M4
Monte Carlo simulation
(5) Iterate (1)–(4) 1,000 times.
, , , …,
<MAM>
M1:
M2:
M3:
M4:
…
<JJA> <SON>
…
M1 (Smallest SBC)
…
(4) Calculate skill score between simulated and observed annual maxima for the validation years
Annual maxima

## Slide 5
II. Modeling procedure — (1) Climate driver selection
Out of 9,023 streamgauges, we first select 8,283 streamgauges where the number of valid iterations ≥ 200.
8,283 sites
Valid iteration: yields positive skill score for annual maxima prediction ().
Iteration 1: > 0 (valid)
Iteration 2: ≤ 0 (invalid)
Iteration 3: > 0 (valid)
…
Iteration 1000: > 0 (valid)
FloodMagnitude_v1.4/01_Covariate_selection/Results02_N_iterations

## Slide 6
II. Modeling procedure — (1) Climate driver selection
For each season, we use the climate drivers as predictors, which are selected at least 70% of valid iterations.
8,283 sites
Valid iteration: yields positive skill score for annual maxima prediction ().
Iteration 1: > 0 (valid)
Iteration 2: ≤ 0 (invalid)
Iteration 3: > 0 (valid)
…
Iteration 1000: > 0 (valid)
e.g.) The number of valid iterations: 430
Valid iteration | DJF model |  |  |  |  |  |  | 
 |  | Tconc | Pprev | Tprev |  | Tconc | Pprev | Tprev
1 | O | X | O | X | X | O | X | X
2 | O | O | X | X | X | O | X | X
3 | O | X | O |  | X | X | O | 
… |  |  |  |  |  |  |  | 
430 | O | O | O | X | X | O | X | X
Percentage | 97% | 50% | 85% | 2% | 0% | 72% | 13% | 1%
Valid iteration | DJF model |  |  |  |  |  |  | 
 |  | Tconc | Pprev | Tprev |  | Tconc | Pprev | Tprev
1 | O | X | O | X | X | O | X | X
2 | O | O | X | X | X | O | X | X
3 | O | X | O |  | X | X | O | 
… |  |  |  |  |  |  |  | 
430 | O | O | O | X | X | O | X | X
Percentage | 97% | 50% | 85% | 2% | 0% | 72% | 13% | 1%
Final DJF model:
FloodMagnitude_v1.4/01_Covariate_selection/Results03_Count_cov_selection
FloodMagnitude_v1.4/ 02_Seasonal_modeling_final / Results01_GAMLSS_Modeling

## Slide 7
II. Modeling procedure — (1) Climate driver selection
For each season, we use the climate drivers as predictors, which are selected at least 70% of valid iterations.
8,283 sites
Valid iteration: yields positive skill score for annual maxima prediction ().
Iteration 1: > 0 (valid)
Iteration 2: ≤ 0 (invalid)
Iteration 3: > 0 (valid)
…
Iteration 1000: > 0 (valid)
e.g.) The number of valid iterations: 430
Valid iteration | MAM model |  |  |  |  |  |  | 
 |  | Tconc | Pprev | Tprev |  | Tconc | Pprev | Tprev
1 | O | X | O | X | X | O | X | X
2 | O | X | X | X | X | O | O | X
3 | O | X | X |  | X | X | O | 
… |  |  |  |  |  |  |  | 
430 | O | O | X | X | X | O | O | X
Percentage | 78% | 20% | 67% | 0% | 5% | 82% | 77% | 1%
Valid iteration | MAM model |  |  |  |  |  |  | 
 |  | Tconc | Pprev | Tprev |  | Tconc | Pprev | Tprev
1 | O | X | O | X | X | O | X | X
2 | O | X | X | X | X | O | O | X
3 | O | X | X |  | X | X | O | 
… |  |  |  |  |  |  |  | 
430 | O | O | X | X | X | O | O | X
Percentage | 78% | 20% | 67% | 0% | 5% | 82% | 77% | 1%
Final DJF model:
Final MAM model:
Final JJA model:
Final SON model:
FloodMagnitude_v1.4/01_Covariate_selection/Results03_Count_cov_selection
FloodMagnitude_v1.4/ 02_Seasonal_modeling_final / Results01_GAMLSS_Modeling

## Slide 8
II. Modeling procedure — (2) Final model fitting and annual maxima simulation
For each season, we fit a statistical model using the entire observation years and the selected climate drivers. Then we conduct Monte Carlo simulation to simulate annual maximum peak discharges.
<Final DJF model>
<Final MAM model>
<Final JJA model>
<Final SON model>
Training years (100%)
Monte Carlo simulation
Distribution of annual maximum peak discharges
e.g.) USGS 11377100
FloodMagnitude_v1.4\04_Evaluation\Results00_Plot_timeseries

## Slide 9
III. Model evaluations
We evaluate our modeling procedure focusing on annual maxima simulation results.
Condition #1. Skill score > 0
e.g.) USGS 11377100 e.g.) USGS 07339000
SS = 0.14
KS.test (Uniform dist.): No
SS = 0.53
KS.test (Uniform dist.): Yes
Condition #2. Non-exceedance probability of observations (KS test)

## Slide 10
III. Model evaluations
We finally select 5,720 streamgauges for further analyses.
Condition #1. Skill score > 0
Condition #2. Non-exceedance probability of observations (KS test)
FloodMagnitude_v1.4/04_Evaluation/